## Slide 1: NET 536 Network Security
Lab 2: TCP IP Attacks ( Indirect)

## Slide 2: Question 1
Using a TCP SYN spoofing attacker, the attacker aims to flood the table of TCP connection requests on a system so that it is unable to respond to legitimate connection requests.
Consider a server system with a table for 256 connection requests. This system will retry sending the SYN-ACK packet five times when it fails to receive an ACK packet in response, at 30 second intervals, before purging the request from its table. Assume that no additional countermeasures are used against this attack and that the attacker has filled this table with an initial flood of connection requests . At what rate ( # of bits per seconds) must the attacker continue to send TCP connection requests to this system in order to ensure that the table remains full? Assuming that the TCP SYN packet is 40 bytes in size.

## Slide 3: Answer Q1
Total time request is in table is ( 30 seconds + 5 attempts to retry)= 180 seconds as there are 256 entries total.
256/180 = 1.42 =~ 2 requests/second
Each request is 40 bytes = 40X8= 320 bits 320X2= 640 bits per secodns
so the attacker needs to send 640 bps to full the table.

## Slide 4: Question 2
Consider a distributed variant of the attack we explore in Lab1. Assume the attacker has compromised a number of broadband-connected residential PCs to use as zombie systems. Also assume each such system has an average uplink capacity of 128 kbps. What is the maximum number 500-byte ICMP echo request (ping) packets a single zombie PC can send per second? How many such zombie systems would the attacker need to flood a target organization using a 0.5-Mbps link, 2-Mbps link, and 10-Mbps link?

## Slide 5: Answer Q2
500 byte message = 4000 bits Uplink capacity of zombie = 128 kbps =128X2^10 = 131072 bits per second # of packet = W/P
= 131072 /4000 = 32.76= 33 packets per second # of zombies = capacity of target system/ capacity of zombies
-To flood 0.5 Mbps : 0.5 Mbps/128 kbps = 0.5x2^20 /128x2^10
=4 zombies
-To flood 2 Mbps : 2 Mbps/ 128 kbps = 2x2^20/ 128x2^10
= 16 zombies
-To flood 10 Mbps : 10 Mbps /128kbps = 10x2^20/ 128x2^10
=80 zombies

## Slide 6: Question 3
In order to implement a DNS amplification attack, the attacker must trigger the creation of a sufficiently large volume of DNS response packets from the intermediary to exceed the capacity of the link to the target organization. Consider an attack where the DNS response packets are 500 bytes in size. How many of these packets per second must the attacker trigger to flood a target organization using a 0.5-Mbps link? 2-Mbps link? 10-Mbps link? If the DNS request packet to the intermediary is 60 bytes, how much bandwidth does the attacker consume to send the necessary rate of DNS request packets for each of these three cases.

## Slide 7: Answer Q3
  DNS Response packet = 500 bytes or 4000 bits # of packets = bandwidth / packets size ( DNS response) For 0.5-Mbps =0.5 X2^20/4000
  = 131.072 =~ 132 packets of DNS response
  For 2-Mbps = 2 X2^20/4000
  =524.288=~ 525 packets of DNS response
  For10-Mbps: 10X2^20/4000
  = 2621.44=~2622 packets of DNS response DNS request = 60 bytes or 480 bits
  Bandwidth of the attacker= # of packets X (DNS request) for 0.5-Mbps: 132 X 480= 63660 bps uplink = 61.8 Kbps for 2-Mbps: 525X 480= 252000 bps uplink = 246 Kbps for 10-Mbps: 2622X480=1258560 bps uplink = 1229 Kbps